## Slide 1
ROBOTICS SOFTWARE — TECHNICAL DEEP DIVE
Autonomous Farm-Lane Navigation
& Plant Counting with a Single RGB-D Camera
Depth-geometric perception · Nav2 · RTAB-Map · ROS 2 Humble
Husky A200
1× RealSense D435
Nav2 (A* + DWB)
RTAB-Map SLAM
0 learned models
Interview presentation — architecture, algorithms, config & reproducibility

## Slide 2
CONTENTS
Agenda
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
1
1 Introduction & problem
2 Evaluation metrics
3 Core design idea
4 System architecture
5 Perception vs. SLAM split
6 Camera intrinsics & calibration
7 RGB-D fusion & TF frames
8 Perception pipeline
9 RANSAC ground plane
10 Obstacle detection
11 Lane detection (bed rows)
12 Plant detection & counting
13 De-duplication logic
14 Localization overview
15 RTAB-Map visual SLAM
16 Nav2 stack & Behavior Tree
17 How A* / NavFn works
18 How DWB works
19 How costmaps work
20 Nav2 config guide
21 Hardcoded vs learned · Q&A

## Slide 3
SECTION 1
Introduction — the task & its hard constraints
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
2
▸ A Husky UGV must drive itself from a BLUE start marker to a GREEN goal marker through a Gazebo farm of irregular, non-parallel crop lanes…
▸ …while detecting and counting the plants it passes.
▸ Four constraints drive every design decision:
  – ONE sensor — a single RealSense RGB-D camera. No LiDAR / 2nd camera / GPS / localization sensor. Wheel odometry (proprioceptive) is allowed.
  – NO colour — HSV / RGB thresholding / green-pixel following = automatic disqualification. Perception must be geometric.
  – NO hardcoded route — real-time planning with ROS 2 Humble + Nav2.
  – Runtime start/goal — marker poses read from the world live, never literals in code.
Why these constraints matter
Single low camera
robot discovers the field incrementally — cannot pre-know lanes
No colour
must infer structure from 3-D geometry (depth), not appearance
No fixed route
navigation must react to what is perceived, frame by frame
Runtime markers
start/goal recovered from Gazebo entity states at launch

## Slide 4
SECTION 2
How the system is scored — four metrics
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
3
01
Navigation success
Reaches the green goal without a navigation failure.
02
Lane coverage
Covered lane area ÷ total lane area × 100. Higher is better.
03
Path efficiency
Distance driven + deviation between planned and actual path.
04
Count accuracy
Estimated vs ground truth — false / missed / duplicate.
DESIGN TARGET
The mission sweeps the field lane-by-lane (coverage) instead of dashing straight to green — directly optimising metric 2 while still terminating at the goal. Plant counting is de-duplicated in a world frame so re-observations never inflate metric 4.

## Slide 5
SECTION 3
Core design idea — perception feeds the costmap, not the wheels
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
4
▸ A robot cannot FOLLOW a lane it has not yet seen — and a hardcoded route is banned.
▸ So lane perception is NEVER a steering signal.
▸ Instead:
  – Depth geometry → an obstacle point cloud.
  – That cloud IS the Nav2 costmap (only obstacle source).
  – Nav2 plans + re-plans a collision-free path to the runtime goal.
  – Motion → new viewpoint → costmap densifies → re-plan. Loop.
▸ Result: fully perception-driven, real-time, no fixed trajectory anywhere in code.
The perception→plan→move loop
Perceive
depth → obstacle cloud
Build costmap
cloud marks cost
Plan & drive
Nav2 A* + DWB
New viewpoint
field revealed further

## Slide 6
SECTION 4
System architecture — dual-branch data flow
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
5
RealSense D435 (RGB-D)
/camera/color · /depth · /camera_info
PERCEPTION BRANCH
lane_perception_node: back-project → RANSAC ground → height classify → bed-row lanes
SLAM BRANCH
RTAB-Map RGB-D SLAM (camera only, 2-D) → drift-corrected map→odom TF
/farm/obstacles (map frame)
the ONLY Nav2 obstacle source
plant_counter_node
count + markers
Nav2 STACK
NavFn A* planner + DWB controller on the perceived costmap
Husky (Gazebo)
planar_move · /cmd_vel
new viewpoint → loop

## Slide 7
SECTION 5
Why perception and SLAM are kept separate
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
6
Perception estimates STRUCTURE
▸ Answers: “where are the beds / plants / free space?”
▸ Output: obstacle cloud + lane centres, per frame.
▸ Depends only on depth geometry.
▸ Swappable: a learned segmentation head could replace it behind the same /farm/obstacles topic.
SLAM estimates POSE
▸ Answers: “where is the robot in the world?”
▸ Output: drift-corrected map→odom transform.
▸ Independent of the obstacle pipeline.
▸ Swappable: any localization (SLAM, AMCL, GPS) can be dropped in without touching perception.
MODULARITY
Decoupling structure-estimation from pose-estimation is the key architectural choice — each can be replaced or upgraded independently.

## Slide 8
SECTION 6
Camera intrinsics & calibration
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
7
Intrinsics (in-sensor)
▸ Horizontal FOV 1.211 rad (≈ 69°); 640 × 480 @ 15 Hz.
▸ Clip range 0.10 – 10 m; Gaussian depth noise σ = 0.005 m.
▸ Gazebo derives fx, fy, cx, cy and publishes them on /camera/depth/camera_info — read LIVE, never hardcoded.
Back-projection (pixel → 3-D)
For each depth pixel (u, v, z):
x = (u − cx) · z / fx
y = (v − cy) · z / fy
z = z
→ organized metric point cloud in the camera optical frame.
INTERVIEW POINT — WHY INTRINSICS MATTER
Intrinsics convert raw pixels + a depth value into metric 3-D. Without correct fx/fy/cx/cy the cloud is geometrically wrong and RANSAC / height thresholds break. In sim they are exact and published on camera_info; on real hardware they come from factory or checkerboard calibration.

## Slide 9
SECTION 7
RGB-D fusion & the extrinsic frame chain
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
8
base_footprint
Nav2 base, planar
base_link
chassis
camera_link
mount: x 0.475, z 0.10, pitch 0.26 rad (~15° down)
camera_depth_optical_frame
REP-103: z-fwd, x-right, y-down
How RGB and depth combine
▸ Extrinsics (URDF joints → TF, via robot_state_publisher) place the metric cloud in a gravity-aligned body/world frame.
▸ This is the calibration that makes “height above ground” physically meaningful.
▸ Depth does ALL decision-making.
▸ RGB is only the canvas for the overlay video — every classified 3-D point carries its source pixel (u,v), so labels can be painted back onto the colour image.
▸ No perception decision ever reads a colour value → the no-HSV rule cannot be violated by construction.

## Slide 10
SECTION 8
Lane / free-space perception — pipeline
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
9
1 Sub-sample & validate
stride 4; drop NaN; keep 0.25–9.0 m
2 Back-project
pixel → 3-D via intrinsics
3 Transform to map
TF: up = real vertical
4 RANSAC ground plane
dominant near-horizontal plane
5 Height classification
drivable vs obstacle
6 Bed-rows → lane centres
+ publish /farm/obstacles
RUNS AT ~6 HZ, PURE PYTHON + NUMPY
Everything is classical geometry — deterministic, dataset-free, auditable. Each stage below is expanded on the next slides.
▸ Synchronised (depth, camera_info, color) triple via ApproximateTimeSynchronizer (0.10 s slop) — RGB carried only for the overlay.

## Slide 11
SECTION 9
RANSAC ground-plane estimation — how & why
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
10
Algorithm (60 iterations)
1. Sample 3 random points → candidate plane n·p + d = 0
2. REJECT if |n·ẑ| < 0.85 (keep near-horizontal only)
3. Count inliers: |n·p + d| < 0.03 m
4. Keep the plane with the most inliers
5. Fallback to flat z = 0 if none found
Points pre-filtered to the low band (map-z < 0.4 m) so the floor dominates the sample.
Why RANSAC (design choice)
▸ Does NOT assume ground = z 0 → robust to camera tilt / mount error / sloped terrain (classifies by signed height above the FITTED plane).
▸ |n·ẑ| > 0.85 gate: beds & plants are outliers and can never win the fit — only the broad farm floor can.
▸ Orientation-invariant → satisfies FR-1 (robust to lane angle, geometry, appearance): a lane at any heading gives the same height signature.
▸ Cheap: 60 iterations on a sub-sampled cloud runs in real time in pure Python.

## Slide 12
SECTION 10
Obstacle detection — height classification
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
11
Signed height h = n·p + d
drivable |h|≤0.06
obstacle 0.10–1.20
foliage 0.28–0.70
▸ Each point classified by SIGNED height above the fitted plane:
  – |h| ≤ 0.06 m → drivable lane surface (GROUND_BAND).
  – 0.10 < h < 1.20 m → obstacle: crop beds (~0.10 m), plants, debris.
▸ Obstacle points → /farm/obstacles as a PointCloud2 in the map frame.
▸ This is the SOLE input to Nav2's obstacle layer — no colour, no LiDAR.
▸ Robot-clear radius drops points too close to the base so it never traps itself in the costmap.
▸ Bed height ≈ 0.10 m and canopy ≈ 0.42 m are the physical facts every threshold is derived from — not fitted to data.

## Slide 13
SECTION 11
Lane detection — bed rows → lane centres
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
12
▸ Within a forward window, obstacle points are projected onto the LATERAL (y) axis.
▸ A 1-D histogram of that projection reveals contiguous peaks = crop-bed rows.
▸ The free-space MIDPOINT between two adjacent rows = a lane centre.
▸ The nearest corridor becomes a look-ahead centreline waypoint (/farm/lane_center), drawn in RViz.
▸ Recomputed every frame → handles irregular, non-parallel, varying-width lanes by construction.
▸ A gap whose bed-spacing is below the pass threshold (the 0.4 m narrow lane) is excluded as non-traversable.
Lateral histogram → lanes
bed
bed
bed
bed
bed
● = lane centre (row midpoint)
obstacle count vs lateral offset y →

## Slide 14
SECTION 12
Plant detection & counting — pipeline
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
13
1 Foliage band
keep 0.28–0.70 m (beds drop out)
2 Grid cluster
0.15 m cells + connected comps
3 Reject non-plants
< 4 pts OR extent > 0.8 m
4 Associate track
nearest < 0.45 m in map frame
5 Confirm & count
≥ 2 hits → count + marker
▸ Subscribes to the SAME obstacle cloud — ground & free space already removed, so only beds + plants remain.
▸ Foliage-height filter keeps the canopy (~0.42 m centre) and removes the 0.10 m beds — pure geometry, no colour.
▸ Elongation guard (extent > 0.8 m) rejects 10 m bed-wall fragments → essentially no false positives.
▸ Ground truth this world: 25 upright (5 beds × 5) + 1 fallen = 26. Fallen plant sits at bed height → known hard miss.

## Slide 15
SECTION 13
De-duplication — counting each plant ONCE
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
14
▸ Every cluster centroid is an OBSERVATION in the drift-corrected map frame.
▸ Because that frame is world-stable, the same physical plant lands at ~same (x, y) from every viewpoint.
▸ Association: match to nearest existing track within 0.45 m →
  – match found → UPDATE that track (running average, weight 1/(obs+1)).
  – none → create a NEW track.
▸ Confirmation: a track is counted only after ≥ 2 observations (kills single-frame flicker).
▸ Seeing a plant 20× → still one track, counted once.
Why r = 0.45 m
▸ Larger than residual inter-viewpoint drift → the SAME plant re-associates.
▸ Smaller than the minimum spacing between DIFFERENT plants → neighbours never merge.
▸ It sits in the sweet spot between those two scales.
▸ Tuning up ⇒ merge risk; tuning down ⇒ duplicate risk.
▸ Entirely geometric — no learned model, no appearance.

## Slide 16
SECTION 14
Localization — odometry + a world-aligned frame
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
15
▸ NO AMCL. AMCL estimates pose from LASER scans — we have no LiDAR, only a depth camera.
▸ odom → base_footprint: from the planar_move drive plugin (wheel/model odometry). Smooth, high-rate, but drifts.
▸ map → odom: drift correction. Two options:
  – RTAB-Map visual SLAM (default) — refines odom with the camera.
  – Static identity transform (use_slam:=false) — map = odom = world, since sim odom is already world-aligned & accurate.
▸ Nav2 plans in map; control executes in odom.
Why no AMCL — talking point
▸ AMCL = particle filter over a KNOWN occupancy grid using laser scans.
▸ No laser → AMCL cannot run.
▸ In simulation the odometry transform is accurate and world-aligned, so a static map→odom is sufficient and stable.
▸ Visual SLAM (RTAB-Map) is the camera-only upgrade that corrects real drift.

## Slide 17
SECTION 15
Visual SLAM — how RTAB-Map is used
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
16
map
world / global
odom
drift accumulates
base_footprint
robot body
camera_depth_optical_frame
sensor
How & why
▸ RGB-D SLAM on the RealSense ALONE. Wheel odom is the motion prior; RTAB-Map refines it with classical visual feature registration + loop closure.
▸ Constrained to 2-D (Reg/Force3DoF, Optimizer/Slam2D) — the farm is planar → far more robust on the low-texture floor.
▸ Reg/Strategy 0 = visual (classical features, NOT a trained network). Vis/MinInliers 10.
▸ Grid/FromDepth = false — the costmap comes from OUR obstacle cloud, not RTAB's grid.
▸ Map origin anchored at the spawn pose → goal_sender converts world coords into map at runtime.
▸ Limitation: on feature-poor floor, loop closure fires rarely → leans on wheel odom. Depth-ICP would be the next upgrade.

## Slide 18
SECTION 16
Nav2 stack & the Behavior Tree
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
17
Goal (runtime marker)
navigate_to_pose
BT Navigator
orchestrates behaviors
Planner Server — NavFn A*
global path
Controller Server — DWB
local trajectory → cmd_vel
Velocity Smoother
limit accel/jerk
Husky
planar_move drive
Behavior Server
spin · backup · wait (recovery)
Why a Behavior Tree?
▸ Each behavior — plan, follow path, recover — is a NODE in a tree, not code in a monolithic state machine.
▸ Modular & easy to extend: add/reorder recovery behaviors without rewriting logic.
▸ BT ticks at ~10 Hz; on planner/controller failure it falls through to Behavior Server recovery (spin, back-up, wait), then retries.
▸ Clean separation: planning ≠ control ≠ recovery.

## Slide 19
SECTION 17
How the global planner works — A* / NavFn
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
18
A* search — the idea
▸ Searches the global costmap grid for the lowest-cost path from robot to goal.
▸ Expands cells by priority f(n) = g(n) + h(n):
  – g(n) = cost so far (distance + costmap cost).
  – h(n) = heuristic (straight-line to goal) — guides search toward the goal.
▸ Admissible heuristic → guaranteed shortest path, far fewer expansions than Dijkstra.
▸ NavFn = Nav2's wavefront/A* planner over the 2-D costmap.
How it's used here
▸ Plugin nav2_navfn_planner/NavfnPlanner, use_astar: true, tolerance 0.5 m.
▸ allow_unknown: true → plans INTO not-yet-seen space and refines as the camera reveals it.
▸ Runs on a rolling global costmap large enough to cover the whole farm.
▸ Obstacle layer marks the perceived beds (clearing off) → routes AROUND discovered dead-ends instead of re-entering.
▸ Re-plans continuously (~2 Hz) as new obstacles appear.

## Slide 20
SECTION 18
How the local controller works — DWB
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
19
DWB = Dynamic Window + critics
▸ Each control cycle (20 Hz) it SAMPLES many (v, ω) velocity commands within the robot's dynamic limits (the “window”).
▸ Each sample is forward-SIMULATED into a short trajectory.
▸ Every trajectory is SCORED by a weighted sum of CRITICS:
  – PathDist / PathAlign — stay on & aligned to the global path.
  – GoalDist / GoalAlign — make progress to the goal.
  – BaseObstacle — penalise collisions; Oscillation — anti-jitter.
▸ Best-scoring trajectory's first command → /cmd_vel.
How it's tuned here
▸ Heavy PathDist / PathAlign weights → the controller HUGS the global path, keeping the 0.67 m skid base centred in ~1 m lanes.
▸ max_vel_x ≈ 0.24, max_vel_theta ≈ 0.8 → stable in tight lanes.
▸ yaw_goal_tolerance wide open — a skid base can't hit an exact final heading, else the goal aborts just short.
▸ Works on the depth-built costmap (which inflates the beds) → far more robust than open-loop lane following.

## Slide 21
SECTION 19
How the costmaps work
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
20
▸ A costmap is a 2-D grid (0.05 m cells) where each cell holds a traversal cost 0–254.
▸ Built from LAYERS composited together:
  – Obstacle layer — marks cells hit by /farm/obstacles points (marking on, clearing off).
  – Inflation layer — spreads a decaying cost around each obstacle so paths keep clearance.
▸ GLOBAL costmap: whole-field, rolling → NavFn plans on it.
▸ LOCAL costmap: small 6×6 m rolling window around the robot → DWB avoids obstacles on it.
▸ Inflation radius 0.36 m ≥ inscribed radius (0.35) → path stays off beds; gentle cost_scaling keeps the lane centre attractive.
Layered composition
Inflation layer
clearance gradient
Obstacle layer
/farm/obstacles marks cost
Static / unknown
free space
Master costmap
planner + controller consume

## Slide 22
SECTION 20
Nav2 configuration guide (nav2_params.yaml)
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
21
Server
Key params
Value / choice
bt_navigator
global_frame / base
map / base_footprint
planner_server
NavFn A*
use_astar, tol 0.5, allow_unknown
controller_server
DWB critics
PathDist/PathAlign high; max_vel_x 0.24, θ 0.8
goal_checker
xy / yaw tol
0.25–0.35 m / open (3.2 rad)
local_costmap
6×6 m, 0.05
obstacle + inflation, rolling
global_costmap
whole field, 0.05
obstacle (clearing off) + inflation
inflation
radius / scaling
0.36 m / 2.8–3.0
obstacle layer
source
/farm/obstacles, marking on, clearing off
velocity_smoother
accel limits
smooth cmd_vel before drive

## Slide 23
SECTION 21
Hardcoded vs learned · interview Q&A
Autonomous Farm-Lane Navigation & Plant Counting · ARTPARK / Versor Round 2
22
Hand-engineered (all of it)
▸ RANSAC ground fit
▸ Height-threshold classify
▸ Histogram bed-row lanes
▸ Grid clustering + tracks
▸ RTAB-Map classical features
▸ NavFn A* + DWB
▸ ~50 constants, 0 learned
Learned — NONE
▸ No HSV / RGB thresholds
▸ No trained network
▸ No colour segmentation
▸ Drop-in later: seg-head behind /farm/obstacles or a detector behind plant tracks — same interface.
Likely questions
Q: Why not AMCL?
A: No laser; sim odom already world-aligned.
Q: Why RANSAC not z=0?
A: Robust to tilt/slope; beds are outliers.
Q: Avoid double counts?
A: Track association in map frame + ≥2 hits.
Q: Why DWB over pure-pursuit?
A: Path-hugging critics keep skid base centred.
Q: Perception steers?
A: No — it feeds the costmap; Nav2 steers.

## Slide 24
Reproduce & key commands
# build image (first run) + launch, headless
cd farm_nav_ws
./run.sh # GUI (Gazebo + RViz)
./run.sh headless:=true use_rviz:=false
# native (Humble on 22.04)
colcon build --symlink-install
source install/setup.bash
ros2 launch farm_bringup bringup.launch.py
# inspect a live run
ros2 topic echo /farm/plant_count
ros2 topic echo /mission/status
KEY FACTS
▸ Launch args: use_rviz · use_slam · headless · spawn_x/y/yaw
▸ Deliverables → ./output : run_video.mp4, path_overlay.png
▸ Ground truth: 26 plants · 4 drivable lanes (0.4 m lane skipped)
▸ Start ≈ (5.8,−3.0) · Goal ≈ (−5.8, 2.7), read at runtime
▸ GPU strongly preferred (software GL times out Nav2 lifecycle)
Depth-geometric · real-time Nav2 · camera-only SLAM · zero learned models — explainable, auditable, reproducible.